Soundgates – Interactive Music Synthesis on FPGAs
 Presentation of the current Prototype
Milestone 2

---
Soundgates – First Prototype
19.11.13
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Outline
- Objectives
  - Milestone 1
  - Milestone 2
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Objectives – Software/Editor
- Milestone 1
  - Basic meta-model
  - Graphical design environment
    - Create and connect components
    - Save and load patch
    - Export to XML
  - Simulation, using Pure Data

---
Objectives – Software/Editor
- Milestone 2
  - Plug in new sound components
  - Code generation Unit (for PureData)
  - Mark input as interactive parameter

---
Objectives – Interaction
- Milestone 2
  - Basic interaction with the hardware
[Speaker Notes: Feature rotary switch dropped]

---
Objectives – Hardware
Milestone 1
  - Wave generators (sine, triangle,...)
  - Basic arithmetic
  - Constants

---
Objectives – Hardware
Milestone 2
  - Set up hardware environment and architecture
  - Set up communication between host PC and ReconOS

---
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Results
- Software
- Interaction
- Hardware

---
Results – Software
Editor
  - Milestone 1 and 2
  - Create composite components
  - Import/Export composite components in a portable format
- ALSA sound output on Zynq
- Wavefile player on Zynq
[Speaker Notes: Italic: features beyond milestone 2]

---
Results – Interaction
Android App to control FPGA inputs
TCP handshake to get adjustable components
OSC protocol via UDP
[Speaker Notes: Italic: features beyond milestone 2]

---
Results – Hardware
Milestone 1 and 2
- Basic components
  - All common wave generators
  - White Noise
  - ADSR and ramp envelope
Shared memory architecture instead of wiring in one single hardware thread
[Speaker Notes: More wave generators than planned Sine Triangle Square Sawtooth Additionally: White noise (realized with random samples) Envelopes ADSR (Attack, Decay, Sustain, Release) Ramp (increasing and decreasing volume) Shared memory architecture]

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
Synthesizer
[Speaker Notes: Example for the architecture Synthesizer as basic, controlling thread]

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
NCO
Synthesizer
write
[Speaker Notes: Synthesizer creates NCO (numeric controlled oscillator) Tells NCO where to write]

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
NCO
Synthesizer
Mixer
write
read
[Speaker Notes: Synthesizer Create mixer Tells mixer where to read]

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
NCO
Synthesizer
Mixer
ALSA
write
read
[Speaker Notes: Synthesizer Tells mixer where to write Tells ALSA buffer where to read]

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
NCO
Synthesizer
Mixer
ALSA
[Speaker Notes: ALSA output]

---
Software / Hardware Threads
- Synthesizer sends start and stop signals
- Thread only processes when requested by synthesizer
[Speaker Notes: Software and hardware thread are treaten equally Same behavior for HW and SW threads Thread gets told when to calc/process data]

---
Software / Hardware Threads
init
Initialize signals / variables

---
Software / Hardware Threads
init
refresh
Refresh user inputs
[Speaker Notes: Read the inputs at the specified adress]

---
Software / Hardware Threads
init
refresh
calc
Check number of samples and write
set of samples to memory
[Speaker Notes: When number of samples hasn't reached maximum number of samples → calculate further data Otherwise → next slide]

---
Software / Hardware Threads
init
refresh
calc
wait
Wait for new start signal

---
Shared Memory Architecture
Pro
No wiring between components
Contra
Timing
 “Layered Shared Memory Architecture”
[Speaker Notes: No wiring inside of a single hardware thread Instead: one hardware thread for one sound component]

---
Layered SHM Architecture
Synthesizer

---
Layered SHM Architecture
HW Thread 1
Synthesizer
HW Thread 2
SW Thread 1
[Speaker Notes: Synthesizer creates layer 1 Layers can consist of HW and SW threads]

---
Layered SHM Architecture
HW Thread 1
Synthesizer
SW Thread 2
HW Thread 2
SW Thread 1
[Speaker Notes: Synthesizer creates threads on layer 2 Again, the layers can contain SW and HW threads]

---
Layered SHM Architecture
HW Thread 1
Synthesizer
SW Thread 2
HW Thread 2
ALSA
SW Thread 1

---
Data Flow
HW Thread 1
SW Thread 2
HW Thread 2
ALSA
SW Thread 1
[Speaker Notes: Architecture data flow]

---
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Toolflow – Overview
- Editor
  - Design of a patch
  - Simulation
- Synthesis
- FPGA execution
[Speaker Notes: Execution order to get running system]

---
Example patch
Sine
Triangle
Wavefile
Mixer
Mixer

---
Example patch
HW
SW
HW
Sine
Triangle
Wavefile
SW
Mixer
SW
Mixer
[Speaker Notes: Hardware: Sine and triangle, Software: Mixer and wavefile player Easy to exchange! For example: Use a SW implementation of sine]

---
Example patch
Sine
Triangle
Wavefile
Mixer
Mixer
Interactive user input
[Speaker Notes: User inputs are independent of HW / SW realization HW and SW threads can be controlled via user input]

---
Example patch
Sine
Triangle
Wavefile
Mixer
Mixer
Interactive user input
bias
bias
frequency
frequency

---
Toolflow – Editor
[Speaker Notes: Screenshot of Editor environment and example patch]

---
Toolflow – Editor Patch
[Speaker Notes: Screenshot of the example patch]

---
Toolflow – Pure Data Export
[Speaker Notes: Example patch exported to and opened in Pure Data Each (composite) component on this screenshot is defined by several other basic components]

---
Toolflow – Pure Data Export
[Speaker Notes: Realization of triangle component]

---
Toolflow – FPGA Execution
[Speaker Notes: Last step in toolflow: execution on FPGA Now: live demo → editor, simulation and FPGA]

---
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Prospect
- Editor
  - Area estimation of (composite) components and COSMIC system
  - System generation
  - Pure Data export compatible with Cycling Max?
- Interaction
  - Advanced sensors on modern Android smartphones (Accelerator, ...)
- Hardware
  - Advanced components (Filters, Amplifier, …)
  - Benchmarking

---
Thank you for your attention
Questions? Comments? Hints?