Soundgates – Interactive Music Synthesis on FPGAs
 Presentation of the current Prototype

---
Soundgates – First Prototype
19.11.13
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Objectives (Milestone 2)
- Editor
  - Plug in new sound components
  - Code generation Unit (for PureData)
  - Mark input as interactive parameter

---
Objectives
- Interaction
  - Adjust a component's parameter via sensor attached to I/O expansion board

---
Objectives
Hardware
  - Set up hardware environment and architecture
  - Set up communication between host PC and ReconOS

---
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Results
- Software
- Interaction
- Hardware

---
Results – Software
Editor
  - Plug in new sound components
  - Code generation Unit (for PureData)
  - Mark input as interactive parameter
  - Create composite components
  - Import/Export composite components in a portable format
- ALSA sound output on Zynq
- Wavefile player on Zynq

---
Results – Interaction
Preliminary Android App to control FPGA inputs
OSC protocol via UDP

---
Results – Hardware
Set up ReconOS environment and hardware architecture
- Basic components
  - Wave generators (Sinus, Sawtooth, Square, Triangle)
  - White Noise
  - ADSR and ramp envelope
Shared memory architecture instead of wiring

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
Main

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
Main
NCO
write

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
Main
NCO
Mixer
Mixer
Mixer
write
read

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
Main
NCO
Mixer
Mixer
Mixer
ALSA
write
read

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
Main
NCO
Mixer
Mixer
Mixer
ALSA
write
read

---
Shared Memory Architecture
Pro
No wiring between components
Contra
Timing
 “Layered Shared Memory Architecture”

---
Layered SHM Architecture
Synthesizer

---
Layered SHM Architecture
HW Thread 1
Synthesizer
HW Thread 2
SW Thread 1

---
Layered SHM Architecture
HW Thread 1
Synthesizer
SW Thread 2
HW Thread 2
SW Thread 1

---
Layered SHM Architecture
HW Thread 1
Synthesizer
SW Thread 2
HW Thread 2
ALSA
SW Thread 1

---
Data Flow
HW Thread 1
Synthesizer
SW Thread 2
HW Thread 2
ALSA
SW Thread 1

---
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Toolflow – Overview
- Editor
  - Design of a patch
  - Simulation
- Synthesis
- FPGA execution

---
Toolflow – Overview
Editor
SCREENSHOT? LIVE DEMO?

---
Toolflow – Overview
PureData Simulation
SCREENSHOT? LIVE DEMO?

---
Toolflow – Overview
Execution on FPGA
  - With interactive input from Android App

---
Live demo

---
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Prospect
- Editor
  - Area estimation of (composite) components and COSMIC system
- Interaction
  - Advanced sensors on modern Androit smartphones (Accelerator, ...)
- Hardware
  - Advanced components (Filters, Amplifier, …)
  - Benchmarking

---
Thank you for your attention
Questions? Comments? Hints?