Soundgates – Interactive Music Synthesis on FPGAs
 Presentation of the current Prototype
Milestone 2

---
Soundgates – First Prototype
19.11.13
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Outline
- Objectives
  - Milestone 1
  - Milestone 2
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Objectives – Software/Editor
- Milestone 1
  - Basic meta-model
  - Graphical design environment
    - Create and connect components
    - Save and load patch
    - Export to XML
  - Simulation, using Pure Data

---
Objectives – Software/Editor
- Milestone 2
  - Plug in new sound components
  - Code generation Unit (for PureData)
  - Mark input as interactive parameter

---
Objectives – Interaction
- Milestone 2
  - Basic interaction with the hardware

---
Objectives – Hardware
Milestone 1
  - Wave generators (sine, triangle,...)
  - Basic arithmetic
  - Constants

---
Objectives – Hardware
Milestone 2
  - Set up hardware environment and architecture
  - Set up communication between host PC and ReconOS

---
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Results
- Software
- Interaction
- Hardware

---
Results – Software
Editor
  - Milestone 1 and 2
  - Create composite components
  - Import/Export composite components in a portable format
- ALSA sound output on Zynq
- Wavefile player on Zynq

---
Results – Interaction
Android App to control FPGA inputs
TCP handshake to get adjustable components
OSC protocol via UDP

---
Results – Hardware
Milestone 1 and 2
- Basic components
  - All common wave generators
  - White Noise
  - ADSR and ramp envelope
Shared memory architecture instead of wiring in one single hardware thread

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
Synthesizer

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
NCO
Synthesizer
write

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
NCO
Synthesizer
Mixer
Mixer
Mixer
write
read

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
NCO
Synthesizer
Mixer
Mixer
Mixer
ALSA
write
read

---
Shared Memory Architecture
Software Threads
SHM
Hardware Threads
NCO
Synthesizer
Mixer
Mixer
Mixer
ALSA
write
read

---
Software / Hardware Threads
- Synthesizer sends start and stop signals
- Thread only processes when requested

---
Software / Hardware Threads
init
Initialize signals/variables

---
Software / Hardware Threads
init
refresh
Refresh inputs

---
Software / Hardware Threads
init
refresh
Calculations
calc

---
Software / Hardware Threads
init
refresh
calc
Check number of samples and
User inputs and write samples
check

---
Software / Hardware Threads
init
refresh
calc
check
wait
Wait for new start signal

---
Shared Memory Architecture
Pro
No wiring between components
Contra
Timing
 “Layered Shared Memory Architecture”

---
Layered SHM Architecture
Synthesizer

---
Layered SHM Architecture
HW Thread 1
Synthesizer
HW Thread 2
SW Thread 1

---
Layered SHM Architecture
HW Thread 1
Synthesizer
SW Thread 2
HW Thread 2
SW Thread 1

---
Layered SHM Architecture
HW Thread 1
Synthesizer
SW Thread 2
HW Thread 2
ALSA
SW Thread 1

---
Data Flow
HW Thread 1
Synthesizer
SW Thread 2
HW Thread 2
ALSA
SW Thread 1

---
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Toolflow – Overview
- Editor
  - Design of a patch
  - Simulation
- Synthesis
- FPGA execution

---
Example patch
Sine
Triangle
Wavefile
Mixer
Mixer

---
Example patch
Sine
Triangle
Wavefile
Mixer
Mixer
Interactive user input

---
Example patch
Sine
Triangle
Wavefile
Mixer
Mixer
Interactive user input
bias
bias
frequency
frequency

---
Toolflow – Overview
Editor

---
Toolflow – Overview
Export to PureData

---
Toolflow – Overview
Execution on FPGA
  - With interactive input from Android App

---
Live demo

---
Outline
- Objectives
- Results
- Toolflow – Overview
- Live demo
- Prospect

---
Prospect
- Editor
  - Area estimation of (composite) components and COSMIC system
  - System generation
- Interaction
  - Advanced sensors on modern Android smartphones (Accelerator, ...)
- Hardware
  - Advanced components (Filters, Amplifier, …)
  - Benchmarking

---
Thank you for your attention
Questions? Comments? Hints?